## Slide 1: Highway Alert System
Alerts for every vehicle on the road, not just one car
Notes: Introduce the project: a highway alert system. One vehicle detects a hazard and the alert is broadcast to every vehicle behind it.

## Slide 2: Why highways need alerts
Sudden stops
A vehicle ahead can brake hard with almost no warning, leaving little time to react.
Damaged roads
Potholes and broken surfaces are hard to see at high speed and can cause loss of control.
Accidents ahead
Drivers often learn about a blocked lane only when they reach it.
Notes: Three real dangers on highways: sudden stops, damaged roads and accidents. Drivers need an early warning.

## Slide 3: What the system warns about
Sudden stop
A vehicle ahead brakes hard. Hard braking is detected.
DANGER red alert
Road damage
Pothole or broken road surface in a lane.
WARNING amber alert
Accident
Crash on the road ahead. The lane may be blocked.
DANGER red alert
Notes: Each hazard has its own icon and alert level. Red means danger, amber means warning.

## Slide 4: New: smarter alerts
Smart lane change
Cars behind a stopped vehicle move to a free lane and keep moving.
SMART keeps moving
Blind person
A blind person is on the road. All vehicles stop and wait.
DANGER red alert
Drunk driver
Alcohol sensor warns all vehicles within 300 m.
DANGER red alert

## Slide 5: How do the other vehicles know?
WITHOUT ALERTS
Each driver sees only the vehicle in front
Reaction takes about 1.4 s
Result: chain crash, 3 vehicles at 90 km/h
WITH BROADCAST ALERTS
The detecting vehicle broadcasts the alert
Every vehicle behind gets it in about 0.25 s
Result: everyone slows early, 0 crashes
Notes: This is the key question. If only one car gets the alert, the cars behind still find out late. With a broadcast, every vehicle behind the hazard is warned at once. The numbers come from the simulation.

## Slide 6: How the alert reaches other vehicles
Detect
A vehicle senses hard braking, a pothole or a crash
Broadcast
It sends a message by V2V radio or the mobile network
Deliver
Every vehicle behind the hazard, within 700 m, receives it
Warn and brake
Banner, beep and voice alert, and the car slows early
Only vehicles behind the hazard, within 700 m, are alerted. Delivery takes about 0.25 s.
Notes: Four steps: detect, broadcast, deliver, warn. In a real system the message goes over V2V radio, 5G or a cloud server like Google Maps.

## Slide 7: What triggers a broadcast
Event | Detected by | Message sent | Who gets it
Sudden stop | Hard braking, more than 6.5 m/s2 | Sudden stop ahead | Vehicles behind, within 700 m
Road damage | First vehicle that comes within 45 m | Road damage ahead | Vehicles behind it
Accident | Crash sensor of the crashed vehicle | Accident ahead | Vehicles behind it
Blind person | Smart cane or camera sees a person on the road | Blind person on road | Vehicles behind, within 700 m
Drunk driver | Alcohol sensor in the car | Drunk driver nearby | All vehicles within 300 m
Notes: Each event has its own detector and its own message. Whoever detects it first sends it to everyone behind.

## Slide 8: Technology used
HTML5 Canvas
Draws the road, vehicles and radar
JavaScript
Moves vehicles and detects dangers
SVG images
Car, truck, pothole and accident art
V2V broadcast
Message to every vehicle behind
Web Audio
Beep sounds for every alert
Voice alerts
Spoken warnings for the driver
Notes: Everything runs in the browser with no extra installation.

## Slide 9: Camera and sensors
Front camera
Proposed: 1080p dashcam to spot people and potholes
Alcohol sensor
In-car sensor (e.g. MQ-3) detects a drunk driver
Smart cane
Blind person’s cane signals nearby cars
Crash sensor
Accelerometer detects a crash or hard braking
GPS
True position and speed of each vehicle
V2V / 5G radio
Sends the alert to vehicles behind
Camera and sensors are proposed hardware. The current demo is a software simulation.

## Slide 10: Hardware prototype
Detect
MPU6050, ultrasonic and MQ-3 sensors detect the danger
Broadcast
An ESP32 board sends an ESP-NOW message to all boards nearby
Deliver
Every other board receives it in milliseconds
Warn
OLED shows the alert, LED lights up, buzzer beeps
Built with ESP32 boards. Range is tens of metres, so it shows the idea, not a road-ready system.
Notes: Hardware prototype: each vehicle is an ESP32 board. Car 1 detects hard braking with an MPU6050 accelerometer, road damage with a button, a person with an ultrasonic sensor on a smart cane, and alcohol with an MQ-3 sensor. It broadcasts the alert with ESP-NOW and the other boards show it on an OLED with an LED and a buzzer. Limits: short range, not real V2X radio, MQ-3 is demo-level, not tested on a real road.

## Slide 11: Results from the simulation
ALERTS OFF
3
vehicles crash
ALERTS ON
0
crashes
Sudden stop at 90 km/h: the truck, You and Car B crash without alerts. An accident ahead gives the same.
At 120 km/h, 4 vehicles crash without alerts. These are simulation results, not real-world data.
Notes: These numbers come from running the simulation with six vehicles. They show the idea, they are not real traffic data.

## Slide 12: Why choose this system?
Warns everyone
One alert reaches every car behind in 0.25 s
Proven result
Simulation: 3 crashes without alerts, 0 with alerts
Keeps moving
Cars change lane instead of all stopping behind
Protects people
Warns cars about a blind person on the road
Drunk driver alert
All vehicles within 300 m are warned
Easy to deploy
Uses the mobile network, no new road gear
Notes: If the client asks 'why should we take this?': 1) One vehicle detects a hazard and every vehicle behind is warned in about 0.25 s, not just one car. 2) In our simulation, a sudden stop at 90 km/h caused 3 crashes without alerts and 0 with alerts. 3) Cars change lane and keep moving instead of everybody stopping. 4) It also protects people: a blind person on the road and a drunk driver nearby are both alerted. 5) It can run over the mobile network, so no new road equipment is needed. Be honest: this is a simulation, and the camera and sensors are proposed hardware.

## Slide 13: Future scope
Google Maps API
Show alerts on a real map with live traffic
Real GPS data
Phone app sends true position and speed
5G and V2X radio
Real vehicle-to-vehicle messages in milliseconds
Camera + AI
Detect potholes, accidents and blind pedestrians automatically
Notes: Next steps to turn the simulation into a real product.

## Slide 14: Conclusion
One vehicle detects the hazard, every vehicle behind is warned
In the simulation, broadcast alerts removed the chain crash
Cars now change lane around a hazard; blind person and drunk driver alerts added
Next: real GPS, maps data and V2X radio
Thank you
Notes: Summarise: the alert is sent to every vehicle behind the hazard, not just one car. Thank the audience and take questions.